## Slide 1: Emission Representation in Energy System Models
Emissions can be fuel-dependent: CO2 emissions can be estimated fairly accurately based on the total amount of fuels combusted and the averaged carbon content of the fuels
1 tonne of bituminous coal
2,563 kg of CO2
Since 1 tonne of coal gives 28.5 GJ
1 PJ of bituminous coal
88 kt of CO2
Notes: https://www.epa.gov/sites/production/files/2015-07/documents/emission-factors_2014.pdf

## Slide 2: Emission Representation in Energy System Models
Emissions can be technology-dependent: Emission factors for NOx depend on the combustion technology and operating conditions and vary significantly, both between individual installations and over time
Source: Ma et al., 2016. Characteristics of NOx emission from Chinese coal-fired power plants equipped with new technologies

## Slide 3: Emission Representation in Energy System Models
Emissions can be technology-dependent: Emission factors for NOx depend on the combustion technology and operating conditions and vary significantly, both between individual installations and over time
Depending on the technology and existence of potential pollution abatement technologies
1 kWh of electricity
X g of NOx