## Slide 1: Defining Renewable Technologies in OSeMOSYS
In OSeMOSYS, solar and wind power plants are characterized by the following parameters:
OutputActivityRatio: defines the rate of fuel provided (i.e. Electricity)
CapitalCost [M$/GW or $/kW]: defines the overnight investment cost of the plant
FixedCost [M$/GW or $/kW]: defines the fixed Operation & Maintenance cost
VariableCost [M$/GWh]: defines the variable costs of the plant
AvailabilityFactor: capacity available on average over one year expressed as a fraction of the total installed capacity, with value ranging from 0 to 1. It gives the possibility to account for planned outages
CapacityFactor: represents the variability in generation of the power plant at each point in time, depending on the availability of resources

## Slide 2: Defining Renewable Technologies in OSeMOSYS
In OSeMOSYS, solar and wind power plants are characterized by the following parameters:
OperationalLife [yr]: defines the lifetime of the technology
Optional:
ResidualCapacity [GW]: defines the existing total capacity available in each year for a specific type of power plant
TotalAnnualMaxCapacity, TotalAnnualMinCapacity [GW]: total maximum/minimum existing (residual plus cumulatively installed) capacity allowed for a technology in a specified year
TotalAnnualMaxCapacityInvestment TotalAnnualMinCapacityInvestment [GW]: maximum/minimum planned new capacity allowed to be installed for a technology in a specified year

## Slide 3: Modelling wind power plant in OSeMOSYS
Wind Power Plant
No input technology
Generation and available power can be “calibrated” by the parameters:
  CapacityFactor
  AvailabilityFactor
The plant can produce at a constant level at any time, as long as the constraints of CapacityFactor and AvailabilityFactor parameters are satisfied
  Therefore, generation pattern is unrestricted (model will tend to use this cheap energy to save on more expensive generation options which does not correspond to real operation)

## Slide 4: Modelling solar in OSeMOSYS
Photovoltaic/CSP
No input technology
Generation and available power can be “calibrated” by:
  CapacityFactor
  AvailabilityFactor
Similar approach to wind
  The parameter CapacityFactor can be used to specify the generation curve of the technology.
  Defining a Storage module (as in the case of hydro dam) can simulate the operational benefits of storage