## Slide 1: Exercise - Learning Objectives
By the end of this exercise you will be able to:
Define the already existing grid network taking centrally generated electricity and distributing it to the final consumer level
Define future expansions of the grid network to enable increased access to electricity

## Slide 2: Defining the grid network
We create a TECHNOLOGY called TD (i.e. Transmission & Distribution).
The following parameters are taken into account
InputActivityRatio: defines the rate of fuel consumed (i.e. Gas)
OutputActivityRatio: defines the rate of fuel provided (i.e. Electricity)
FixedCost: defines the fixed Operation & Maintenance cost ($M/GW or $/kW)
OperationalLife: defines the lifetime of the technology (in years)
CapacitytoActivityUnit: defines how much activity can occur by one unit of capacity in one year (in this case we are using GW for capacity and PJ for energy, thus 1 GW can provide 31.536 PJ annually)
Notes: CapacityToActivityUnit: 1 GW (installed capacity) x 8760 h/yr = 8760 GWh → Activity per year = 31.536 PJ
CapacityToActivityUnit → TotMaxCapacity = GW * 8760h * 1yr * ConversionUnit (PJ/GW) → (it is a conversion factor) 8760 GWh = 31.536 PJ

## Slide 3: Defining characteristics of the grid network
For the TD technology, let’s define the following.
InputActivityRatio: Choose the SEC_EL fuel and insert the following for mode of operation 1.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 4: Defining characteristics of the grid network
For the TD technology, let’s define the following.
OutputActivityRatio: Choose the FEL1 fuel and insert the following for mode of operation 1.
Note that Input/OutputActivityRatio define efficiency: 95%
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95

## Slide 5: Defining characteristics of the grid network
For the TD technology, let’s define the following.
FixedCost: Insert the following values.
The OperationalLife can be set to 50 years, while the CapacitytoActivityUnit can be set to 31.536.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
TD | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
TD | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
TD | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96

## Slide 6: Defining an expansion of the grid network
We continue to create a TECHNOLOGY called GridExp (i.e. Grid Expansion for the purpose of increasing electricity access).
The following parameters are taken into account
InputActivityRatio: defines the rate of fuel consumed (i.e. Gas)
OutputActivityRatio: defines the rate of fuel provided (i.e. Electricity)
FixedCost: defines the fixed Operation & Maintenance cost ($M/GW or $/kW)
CapitalCost: defines the overnight investment cost ($M/GW or $/kW)
OperationalLife: defines the lifetime of the technology (in years)
CapacitytoActivityUnit: defines how much activity can occur by one unit of capacity in one year (in this case we are using GW for capacity and PJ for energy, thus 1 GW can provide 31.536 PJ annually)
Notes: CapacityToActivityUnit: 1 GW (installed capacity) x 8760 h/yr = 8760 GWh → Activity per year = 31.536 PJ
CapacityToActivityUnit → TotMaxCapacity = GW * 8760h * 1yr * ConversionUnit (PJ/GW) → (it is a conversion factor) 8760 GWh = 31.536 PJ

## Slide 7: Defining characteristics of the grid network
For the GridExp technology, let’s define the following.
InputActivityRatio: Choose the SEC_EL fuel and insert the following for mode of operation 1.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 8: Defining characteristics of the grid network
For the GridExp technology, let’s define the following.
OutputActivityRatio: Choose the FEL2 fuel and insert the following for mode of operation 1.
Note that Input/OutputActivityRatio define efficiency: 82%
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82 | 0.82

## Slide 9: Defining characteristics of the grid network
For the GridExp technology, let’s define the following.
FixedCost: Insert the following values.
The OperationalLife can be set to 50 years, while the CapacitytoActivityUnit can be set to 31.536.
 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
GridExp | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
GridExp | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
GridExp | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96

## Slide 10: Defining characteristics of the grid network
For the GridExp technology, let’s define the following.
CapitalCost: Insert the following values.
Note that this is a simplification, based on assumptions! Grid expansion cost typically depends on the distance (hence the importance of geospatial electrification toolkits – e.g. OnSSET)
 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
GridExp | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
GridExp | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
GridExp | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000