## Slide 1: Thermal power plants in the RES
Resources
Primary
Secondary
Final

## Slide 2: Thermal power plants in the RES
Resources
Primary
Secondary
Final

## Slide 3
Coal
Coal-fired Power Plant
Biomass/Waste
Electricity
Biomass-fired Power Plant
Heavy fuel oil
Oil-fired Power Plant
Examples
Natural gas
Natural gas-fired Power Plant
Diesel
Diesel-fired Power Plant / Engine
Electricity
Electricity
Electricity
Electricity

## Slide 4: Sample characteristics of thermal power plants
Coal
Coal-fired Power Plant
Electricity
Best Available Technology | 
Capital cost | 2200 $/kW
VOM and FOM cost | 88 $/kW/a
Capacity Factor | 75-80%
Efficiency | 46%
Integrated Gasification Combined Cycle | 
Capital cost | 3700 $/kW
VOM and FOM cost | 148 $/kW/a
Capacity Factor | 75-80%
Efficiency | 46%
Source: ETSAP.
Notes: ETSAP = Energy Technology Systems Analysis Program

## Slide 5: Sample characteristics of thermal power plants
Natural gas
Natural gas-fired Power Plant
Electricity
OCGTs | 
Capital cost | 900 $/kW
VOM and FOM cost | 36 $/kW/a
Lifetime | 30 years
Efficiency | 35-42%
CCGTs | 
Capital cost | 1100 $/kW
VOM and FOM cost | 44 $/kW/a
Lifetime | 30 years
Efficiency | 52-60%
Source: ETSAP.
Notes: OCGT Open Cycle Gas Turbine
CCGT Combined Cycle Gas Turbine

## Slide 6: Sample characteristics of thermal power plants
Heavy fuel oil
Oil-fired Power Plant
Electricity
HFO Gas Turbines | 
Capital cost | 1490 $/kW
Efficiency | 35%
Diesel generators | 
Capital cost | 780 $/kW
FOM cost | 8 $/kW/a
Efficiency | 35%
Diesel
Diesel-fired Power Plant / Engine
Electricity
Source: ETSAP.

## Slide 7: Sample characteristics of thermal power plants
Biomass
Biomass-fired Power Plant
Electricity
Biomass CHP plant | 
Capital cost | 3000-6000 $/kW
FOM cost | 100 $/kW/a
Fuel cost | 30-50 $/MWh
Electric Efficiency | 16-36%
Totall Efficiency | 40-85%
Source: ETSAP.