## Slide 1: Exercise - Learning Objectives
By the end of this exercise you will be able to:
Define technologies representing domestic production of energy commodities
Define technologies representing import of energy commodities

## Slide 2
Natural Gas Imports
Natural Gas Production
Natural Gas
Wind
New CCGT/GT
Hydro run-of-river
Hydro Dam
Demand for electrified population
Transmission & Distribution
Dist. Solar PV
Dist. Solar PV with battery
Grid Expansion
Demand for future connections
Backstop 1
Backstop 2

## Slide 3
Natural Gas Imports
Natural Gas Production
Natural Gas
Wind
New CCGT/GT
Hydro run-of-river
Hydro Dam
Demand for electrified population
Transmission & Distribution
Dist. Solar PV
Dist. Solar PV with battery
Grid Expansion
Demand for future connections
Backstop 1
Backstop 2

## Slide 4: Defining primary energy forms
The first step in defining the supply of energy forms is the creation of the respective fuels. In this example, we will look at natural gas.
Create a new FUEL called Gas.

## Slide 5: Defining characteristics of the supply
Then, we have to create a TECHNOLOGY called GasExtraction.
In order to represent the technology appropriately, the following parameters have to be taken into account
OutputActivityRatio: defines the fuel provided (in this case Gas)
VariableCost: defines the cost of extraction
TotalTechnologyModelPeriodActivityUpperLimit: defines the level of proven gas reserves that are available for extraction throughout the entire model period (we will express it in PJ)
TotalAnnualMaxCapacity: defines the maximum annual rate of production

## Slide 6: Defining characteristics of the supply
For the GasExtraction technology, let’s define the following.
OutputActivityRatio: Choose the Gas fuel and insert the following for mode of operation 1.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 7: Defining characteristics of the supply
For the GasExtraction technology, let’s define the following.
VariableCost: Insert the following for mode of operation 1.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 8 | 8 | 8
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 8 | 8 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 9 | 9
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 9 | 9 | 9 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 10

## Slide 8: Defining characteristics of the supply
For the GasExtraction technology, let’s define the following.
TotalAnnualMaxCapacity: Insert the following values to limit the production of natural gas.
The TotalTechnologyModelPeriodActivityUpperLimit can be set to 125.
 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
GasEx | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
GasEx | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
GasEx | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6

## Slide 9: Defining characteristics of the supply
Then, we have to create a TECHNOLOGY called GasImport.
In order to represent the technology appropriately, the following parameters have to be taken into account
OutputActivityRatio: defines the rate of fuel provided (in this case Gas)
VariableCost: defines the cost of extraction

## Slide 10: Defining characteristics of the supply
For the GasImport technology, let’s define the following.
OutputActivityRatio: Choose the Gas fuel and insert the following for mode of operation 1.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 11: Defining characteristics of the supply
For the GasImport technology, let’s define the following.
VariableCost: Insert the following for mode of operation 1.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 8 | 8 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 9 | 9
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 9 | 9 | 9 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 10
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 10 | 10 | 10 | 10.5 | 10.5 | 10.5 | 10.5 | 10.5 | 11