## Slide 1: Exercise - Learning Objectives
By the end of this exercise you will be able to:
Define Solar PV technology generating electricity at the decentralized level, along with a temporal profile of generation
Define Solar PV technology, coupled with a battery, generating electricity at the decentralized level, along with an assumed temporal profile of generation
Run the model and check results on production by technology and capacity of each technology

## Slide 2
Natural Gas Imports
Natural Gas Production
Natural Gas
Wind
New CCGT/GT
Hydro run-of-river
Hydro Dam
Demand for electrified population
Transmission & Distribution
Dist. Solar PV
Dist. Solar PV with battery
Grid Expansion
Demand for future connections
Backstop 1
Backstop 2
Electricity

## Slide 3
Natural Gas Imports
Natural Gas Production
Natural Gas
Wind
New CCGT/GT
Hydro run-of-river
Hydro Dam
Demand for electrified population
Transmission & Distribution
Dist. Solar PV
Dist. Solar PV with battery
Grid Expansion
Demand for future connections
Backstop 1
Backstop 2
Electricity

## Slide 4: Defining a solar technology
We continue to create a TECHNOLOGY called SOLPV1 (i.e. solar PV rooftop).
The following parameters are taken into account
OutputActivityRatio: defines the rate of fuel provided (i.e. Electricity)
VariableCost: defines the variable Operation & Maintenance cost ($M/PJ or $/GJ)
CapitalCost: defines the overnight investment cost of the plant ($M/GW or $/kW)
CapacityFactor: represents the variability in generation at each point in time.
OperationalLife: defines the lifetime of the technology (in years)
CapacitytoActivityUnit: defines how much activity can occur by one unit of capacity in one year (in this case we are using GW for capacity and PJ for energy, thus 1 GW can provide 31.536 PJ annually)

## Slide 5: Defining a solar technology
For the SOLPV1 technology, let’s define the following.
OutputActivityRatio: Choose the FEL2 fuel and insert the following for mode of operation 1.
Note that for RET, we don’t need to define an input fuel
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 6: Defining a solar technology
For the SOLPV1 technology, let’s define the following.
VariableCost: Insert the following for mode of operation 1.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5

## Slide 7: Defining a solar technology
For the SOLPV1 technology, let’s define the following.
CapitalCost: Insert the following values.
The OperationalLife can be set to 25 years, while the CapacitytoActivityUnit can be set to 31.536.
 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
SOLPV1 | 1700 | 1700 | 1700 | 1700 | 1700 | 1700 | 1600 | 1600 | 1600
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
SOLPV1 | 1600 | 1600 | 1500 | 1500 | 1500 | 1500 | 1500 | 1400 | 1400
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
SOLPV1 | 1400 | 1400 | 1400 | 1300 | 1300 | 1300 | 1300 | 1300 | 1200

## Slide 8: Solar variability in generation
Chart: PV Capacity Factor
| 0 | 2.0833333333333301E-2 | 4.1666666666666699E-2 | 6.25E-2 | 8.3333333333333301E-2 | 0.104166666666667 | 0.125 | 0.14583333333333301 | 0.16666666666666699 | 0.1875 | 0.20833333333333301 | 0.22916666666666699 | 0.25 | 0.27083333333333298 | 0.29166666666666702 | 0.3125 | 0.33333333333333298 | 0.35416666666666702 | 0.375 | 0.39583333333333298 | 0.41666666666666702 | 0.4375 | 0.45833333333333298 | 0.47916666666666702 | 0.5 | 0.52083333333333304 | 0.54166666666666696 | 0.5625 | 0.58333333333333304 | 0.60416666666666696 | 0.625 | 0.64583333333333304 | 0.66666666666666696 | 0.6875 | 0.70833333333333304 | 0.72916666666666696 | 0.75 | 0.77083333333333304 | 0.79166666666666696 | 0.8125 | 0.83333333333333304 | 0.85416666666666696 | 0.875 | 0.89583333333333304 | 0.91666666666666696 | 0.9375 | 0.95833333333333304 | 0.97916666666666696
Mar | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0020041 | 0.015608 | 0.071695 | 0.16666 | 0.28601 | 0.3885 | 0.45636 | 0.52893 | 0.58842 | 0.61274 | 0.62928 | 0.67225 | 0.63875 | 0.62454 | 0.56744 | 0.50098 | 0.4847 | 0.38901 | 0.35301 | 0.29541 | 0.24943 | 0.18871 | 0.11703 | 0.037573 | 0.004977 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Jun | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00030172 | 0.010053 | 0.026469 | 0.044956 | 0.14825 | 0.24029 | 0.32347 | 0.40349 | 0.49027 | 0.55218 | 0.57057 | 0.64304 | 0.69252 | 0.73067 | 0.75234 | 0.76024 | 0.71822 | 0.69617 | 0.64363 | 0.58392 | 0.51288 | 0.4753 | 0.4182 | 0.33866 | 0.25787 | 0.1872 | 0.11192 | 0.054569 | 0.02518 | 0.0045943 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sep | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00026057 | 0.0096823 | 0.039319 | 0.18038 | 0.29264 | 0.40522 | 0.49059 | 0.55649 | 0.59118 | 0.65656 | 0.67916 | 0.6892 | 0.70754 | 0.71404 | 0.68492 | 0.66837 | 0.63399 | 0.60803 | 0.57083 | 0.51768 | 0.42394 | 0.33149 | 0.23258 | 0.1391 | 0.05254 | 0.0089692 | 0.00032914 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 9: Solar variability in generation
For the SOLPV1 technology, let’s define the following.
CapacityFactor: Insert the following values for the entire modelling period.
ID | 0.3
IN | 0
SD | 0.4
SN | 0
WD | 0.25
WN | 0

## Slide 10: Run the model and check the results!

## Slide 11: Defining a solar technology
We continue to create a TECHNOLOGY called SOLPV2 (i.e. solar PV rooftop with battery).
The following parameters are taken into account
OutputActivityRatio: defines the rate of fuel provided (i.e. Electricity)
VariableCost: defines the variable Operation & Maintenance cost ($M/PJ or $/GJ)
CapitalCost: defines the overnight investment cost of the plant ($M/GW or $/kW)
CapacityFactor: represents the variability in generation at each point in time.
OperationalLife: defines the lifetime of the technology (in years)
CapacitytoActivityUnit: defines how much activity can occur by one unit of capacity in one year (in this case we are using GW for capacity and PJ for energy, thus 1 GW can provide 31.536 PJ annually)

## Slide 12: Defining a solar technology
For the SOLPV2 technology, let’s define the following.
OutputActivityRatio: Choose the FEL2 fuel and insert the following for mode of operation 1.
Note that for RET, we don’t need to define an input fuel
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 13: Defining a solar technology
For the SOLPV2 technology, let’s define the following.
VariableCost: Insert the following for mode of operation 1.
Mode | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
1 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
1 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
1 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5

## Slide 14: Defining a solar technology
For the SOLPV2 technology, let’s define the following.
CapitalCost: Insert the following values.
The OperationalLife can be set to 25 years, while the CapacitytoActivityUnit can be set to 31.536.
 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
SOLPV2 | 2700 | 2700 | 2700 | 2700 | 2700 | 2700 | 2600 | 2600 | 2600
 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
SOLPV2 | 2600 | 2600 | 2500 | 2500 | 2500 | 2500 | 2500 | 2400 | 2400
 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
SOLPV2 | 2400 | 2400 | 2400 | 2300 | 2300 | 2300 | 2300 | 2300 | 2200

## Slide 15: Defining a solar technology
For the SOLPV2 technology, let’s define the following.
CapacityFactor: Insert the following values for the entire modelling period.
Note that we assume a fixed profile for discharging of the battery (i.e. simplification)
ID | 0.25
IN | 0.12
SD | 0.3
SN | 0.15
WD | 0.2
WN | 0.1

## Slide 16: Run the model and check the results!