## Slide 1: Defining Hydropower Generation Technologies (Hydro Dam) in OSeMOSYS
Two technologies to be characterized:
River = primary resource
Hydropower plant = electricity generation (transformation) technology
Dam = storage technology
Hydropower
Secondary Electricity
River
Water
Dam
Notes: Modelling hydro dams is slightly more complex than modelling Run-Of-River power plants. Let’s therefore first have a look on what technologies and fuels are needed in OSeMOSYS to represent a hydro dam.
In total two technologies, one storage unit and two fuels are needed.
The first technology can be called river and represents the source of water. The second technology, here called ‘Hydropower’, can either fill the dam or use the stored water from the dam to generate electricity.
The detailed parameterisation will be described on the following slides.

## Slide 2: Defining Hydropower Generation Technologies (Hydro Dam) in OSeMOSYS
In OSeMOSYS, hydro dams are characterized by the following parameters:
For the River:
OutputActivityRatio: defines the output of the technology (i.e. Water)
CapacityFactor: represents the variability in water flow throughout the year
TotalAnnualMaxCapacity, TotalAnnualMinCapacity [GW]: defines the maximum/minimum rate of water flow.
Optional:
TotalTechnologyAnnualActivityUpperLimit [PJ]: defines the (estimated) maximum volume of water going through the river in each year
Notes: The definition of the technology that represents the river doesn’t require the use of many parameter.
The OutputActivityRatio is set to 1 for the fuel ‘water’ to indicate that the output of the technology is water.
With the CapacityFactor the availability of water is considered.
Important to define is also the TotalAnnualMaxCapacity since it indicates the size of the river, which of course is not increasable.
Additionally there is also the option to limit the total annual flow of the river by using the parameter TotalTechnologyAnnualActivityUpperLimit.

## Slide 3: Defining Hydropower Generation Technologies (Hydro Dam) in OSeMOSYS
In OSeMOSYS, hydro dams are characterized by the following parameters:
For the Hydropower plant:
InputActivityRatio: defines the rate of fuel consumed (i.e. Water)
OutputActivityRatio: defines the rate of fuel provided (i.e. Stored_Energy and Electricity); in this case 2 modes of operation are considered: one for storing energy to the dam, one to provide electricity to the grid.
CapitalCost [M$/GW or $/kW]: defines the overnight investment cost of the plant
FixedCost [M$/GW or $/kW]: defines the fixed Operation & Maintenance cost
VariableCost [M$/GWh]: defines the variable costs of the plant
AvailabilityFactor: capacity available on average over one year expressed as a fraction of the total installed capacity, with value ranging from 0 to 1. It gives the possibility to account for planned outages.
OperationalLife [yr]: defines the lifetime of the technology
Notes: Hydro power plants can either store/hold back the water that comes from the river or they can let it run through and produce electricity.
To represent this in OSeMOSYS we need to use the feature of defining more than one ModeOfOperation. I.e. one mode for filling the reservoir, and one mode for producing electricity.
Let’s say in mode of operation 1 we are filling the reservoir with the water from our river technology. To do so we define the InputActivityRatio for the fuel water and the OutPutActivityRatio for the fuel ‘StoredEnergy’. To produce electricity in Mode of operation 2 we set the OutputActivityRatio for Electricity to 1.
As for other technologies we also need to implement the CapitalCost, the FixedCost, the VariableCost (if applicable), the AvailabilityFactor – to account for planned outages, and the OperationalLife to indicate the technical lifetime.

## Slide 4: Defining Hydropower Generation Technologies (Hydro Dam) in OSeMOSYS
In OSeMOSYS, hydro dams are characterized by the following parameters:
For the Hydropower plant:
TechnologyToStorage: binary parameter linking the technology to the storage facility it charges
TechnologyFromStorage: binary parameter linking the storage facility to the technology it feeds
TotalAnnualMaxCapacity, TotalAnnualMinCapacity [GW]: total maximum/minimum existing (residual plus cumulatively installed) capacity allowed for a technology in a specified year.
Optional:
ResidualCapacity [GW]: defines the existing total capacity available in each year for a specific type of power plant.
TotalAnnualMaxCapacityInvestment TotalAnnualMinCapacityInvestment [GW]: maximum/minimum planned new capacity allowed to be installed for a technology in a specified year.
Notes: Continuing the set-up of our hydropower plant we need to define the parameter TechnologyToStorage and TechnologyFromStorage. The former needs to be set to 1 for the technology that is charging a specific storage unit and the latter for the technology that is discharging the storage.
Since the options to install hydro power dams are usually rather limited it is also important to define the TotalAnnualMaxCapacity according to the potential.
Optionally it is also possible to consider existing power plants by defining the parameter ResidualCapacity. In case that new capacity is expected to be installed or that the only a limited amount of capacity can be installed per year the parameter TotalAnnualMaxCapacityInvestment and TotalAnnualMinCapacityInvestment can be used to indicate the minimum or the maximum amount of capacity that needs to be or that can be installed within one year.

## Slide 5: Defining Hydropower Generation Technologies (Hydro Dam) in OSeMOSYS
In OSeMOSYS, hydro dams are characterized by the following sets and parameters:
For the Dam (storage):
SETS
SEASON: one per each season considered in the model, named with consequential numbers.
DAYTYPE: one set per each day type represented in the model , named with consequential numbers.
DAILYTIMEBRACKET: one set per each daily time slice represented in the model , named with consequential numbers.
Notes: After defining the river technology and the hydropower technology which serves the purpose of filling and discharging the reservoir and producing electricity, we need to define the storage unit.
The first step for including storage is to define three new SETS. This is necessary to be able to indicate the model the sequence of the TimeSlices.
The first set to be defined are the seasons. Each season considered in the model needs to be put in the set SEASON with consequential numbers.
In the next step the DAYTYPES considered need to be implemented in the SET Daytypes. This is to indicate how many different days we consider per season. This should be done with consequential numbers as well.
Lastly we define the DAILYTIMEBRACKETS. Here we create one per time slice in the model.

## Slide 6: Defining Hydropower Generation Technologies (Hydro Dam) in OSeMOSYS
In OSeMOSYS, hydro dams are characterized by the following sets and parameters:
For the Dam (storage):
Parameters
Conversionls, Conversionld, Convrsionlh: binary parameters used to identify the time slices of each season, day-type and daily time bracket respectively, and to define the temporal sequence of time slices in the model.
StorageLevelStart [PJ]: defines the starting level of the storage at the first year of modelling
StorageMaxChargeRate [GW]: defines the maximum rate at which the storage can charge
StorageMaxDischargeRate [GW]: defines the maximum rate at which the storage can discharge
MinStorageCharge: defines the level to which the storage can be emptied
CapitalCostStorage [M$/GW or $/kW]: defines the overnight cost of investment of the storage
ResidualStorageCapacity [GW]: defines the existing capacity of the storage
OperationalLifeStorage [yr]: defines the lifetime of the storage
Notes: After defining the necessary SETS on the previous slide the necessary parameter need to be defined. The Conversionls, Conversionld and Conversionlh are used to indicate which TimeSlice belong to which season, DayType, and DailyTimeBracket respectively.
Furthermore, there are the storage specific parameter StorageLevelStart, StorageMaxChargeRate, StorageMaxDischargeRate, MinStorageCharge. These are used to characterize the technical specifications of the storage.
Smiliar to technologies storage has the parameter CapitalCostStorage, ResidualStorageCapacity and OperationalLifeStorage. These parameter allow to consider the storage independently from the charging and discharging technology.