## Slide 1: Defining Hydropower Generation Technologies (Run-Of-River) in OSeMOSYS
In OSeMOSYS, hydropower plants (Run-Of-River) are characterized by the following parameters:
OutputActivityRatio: defines the rate of fuel provided (i.e. Electricity)
CapitalCost [M$/GW or $/kW]: defines the overnight investment cost of the plant
FixedCost [M$/GW or $/kW]: defines the fixed Operation & Maintenance cost
VariableCost [M$/GWh]: defines the variable costs of the plant
AvailabilityFactor: capacity available on average over one year expressed as a fraction of the total installed capacity, with value ranging from 0 to 1. It gives the possibility to account for planned outages.
Hydro
Run-Of-River
Secondary Electricity
Notes: The figure on this slide indicates that for modelling Run-Of-River power plants we need to define and consider the technology ‘Hydro Run-Of-River’ and the fuel ‘Secondary Electricity’.
These are related by setting the OutputActivityRatio in the technology ‘Hydro Run-Of-River’ to 1 for the fuel ‘Secondary Electricity’. The technology is then defined by inserting data for the parameter listed on this and the next slide. I will now go over them and comment them.
We define the OutputActivityRatio to 1 for secondary electricity as mentioned above.
The CapitalCost represent the investment cost related to the technology. These occur only once in the technology lifetime.
The FixedCost are reflecting the cost related to the operation and maintenance of the power plant and are defined per kW or GW and year.
VariableCost are representing cost that occur only while the technology is under operation. For hydro power plants these are often 0, but it depends on the reporting scheme.
The AvailabilityFactor has been described in a previous section of this module. However, it is used to indicate the share of time on a scale of 0 to 1 in which the technology is available for production. This is to consider planed outages for example for maintenance.

## Slide 2: Defining Hydropower Generation Technologies (Run-Of-River) in OSeMOSYS
In OSeMOSYS, hydropower plants (Run-Of-River) are characterized by the following parameters:
CapacityFactor: represents the variability in generation of the power plant at each point in time, depending on the availability of resources.
CapacityToActivityUnit: defines how much activity can occur by one unit of capacity in one year
OperationalLife [yr]: defines the lifetime of the technology
Optional:
ResidualCapacity [GW]: defines the existing total capacity available in each year for a specific type of power plant.
TotalAnnualMaxCapacity, TotalAnnualMinCapacity [GW]: total maximum/minimum existing (residual plus cumulatively installed) capacity allowed for a technology in a specified year.
TotalAnnualMaxCapacityInvestment TotalAnnualMinCapacityInvestment [GW]: maximum/minimum planned new capacity allowed to be installed for a technology in a specified year.
Notes: Three more parameter that are essential to define Run-Of-River hydro power plants are the CapacityFactor, the CapacityToActivityUnit and the OperationalLife.
The CapacityFactor has been discussed before, it indicates the availability of the technology in a certain TimeSlice. In the context of hydro power this refers to the availability of water.
The CapacityToActivityUnit defines how much activity can occur by one unit of capacity in one year. In our model we are using GW for capacity and PJ for energy, thus 1 GW can provide 31.536 PJ annually, which means that we set the CapacityToActivityUnit to 31.536 as for every other power generating unit in our model.
The OperationalLife is used to indicate how long a technology is usable after installing it. This means we are indicating the technical lifetime.
Apart from the parameter that need to be defined there are a couple of parameter that can be optionally defined if needed.
The parameter ResidualCapacity can be used to consider power plant capacities that are already installed in the represented energy system.
The two parameter TotalAnnualMaxCapacity and TotalAnnualMinCapacity can be used to set an upper or lower limit concerning the installed capacity of the technology.
With the two parameter TotalAnnualMaxCapacityInvestment and TotalAnnualMinCapacityInvestment the installation of new capacity can be limited or forced in on an annual base.